## Slide 1: Geolux Hydrology Systems
www.geolux-radars.com
Roundtable: Innovative Solutions for the Sustainability of the Adriatic Sea| Zadar | 27 April 2021

## Slide 2: Geolux d.o.o.
from 2007
R&D oriented company specialized for sensors
Radar technology experts
Industrial, environmental, security and traffic applications
R&D and manufacturing in EU
Hidrology
Complete solution for level & flow monitoring
Rivers, channels, wastewater, lakes and hydropower
Radar level metering
Radar surface velocity metering
Additional water quality sensors possible
Data logger (GPRS / NB Iot / LoRaWAN / Sigfox / EUMETSAT / IRIDIUM)
Cloud based software HydroView for real time analytics

## Slide 3: Hydrology Instruments – radar based
RSS-2-300W Radar surface velocity meter
Mounted above water with no contact with water
SDR (Software Defined Radio) designed with advanced digital signal processing for accurate and robust measurements in all conditions
Wide measurement range from 0,02m/s to 15m/s
High sensitivity enable mounting on distance up to 50m effective distance from radar to water surface
METAS certificate, <1% uncertainty
LX-80 Radar level meter
Narrow beam antenna <2°
Level measurement up to 35m with ±1mm accuracy
Liquid and solid objects classification (detection)
Ice, snow, sand level measurement
Snow packing factor (density) measurement in R&D

## Slide 4: Hydrology Instruments – radar based
RSS-2-300WL Radar discharge measurement
Mounted above water with no contact with water
Combining RSS-2-300W & LX-80 instruments
Integrated advanced CFD model for flow calculation in open channels, wastewater, industrial applications, irrigation etc.
SmartObserver Logger
Robust data logger for hydrology systems
Very low power and integrated battery charger
Advanced CFD calculation of flow with multiple sensors for complex situations

## Slide 5: Applications on sea

## Slide 6: Applications on sea – HydroView Cloud Software

## Slide 7: Applications on sea
Multiple depth sea temperature real time measurement
Salinity and many other parameters measurement
Meteorological sensor integrated to the station
Minimal maintenance
No problems with material buildup, organic deposition, oxidation…
Long term measurement stability

## Slide 8: Industrial applications
Measurement of velocity and direction (0,02m/s to 15m/s)
Resolution of 5mm/s
Measurement of level (15m / ±1mm or 5m / ±0,1mm)
IP68 robust design – possible air and water cooling
High temperature (~1800°C)
Low temperature (<-100°C)
Aggressive atmosphere
High pressure

## Slide 9: Security and defense applications
Ground surveillance 3D FMCW radar
100mW K-band (24GHz) with range up to 300m for single walking human (0,75m2 RCS)
MIMO digital beamforming - no moving parts
combined FPGA & DSP architecture
Detection, location and countermeasures control

## Slide 10: Technology
In-house R&D
Microwave electronics and communication systems
Microwave antenna design
Embedded and processing electronics design
Signal processing software development
Very good RF laboratory, electronics laboratory, hydrology laboratory

## Slide 11
Thank You!
Geolux success story @ Altium booth on EmbeddedWorld 2017
Geolux selected among most innovative companies in Croatia by Croatian SME agency HAMAG-BICRO
Geolux success story presented by European Comission in 2018